## Slide 1: Gravitational Waves: Experimental Techniques
Gabriele Vajente
LIGO Laboratory – California Institute of Technology
TRISEP 2018 - Perimeter Institute
1

## Slide 2: Outline
Lecture 1: the basics of interferometric detection of gravitational waves
Lecture 2: fundamental noise sources (seismic, thermal and quantum noises)
Lecture 3: the dirty reality of ”technical noises” (scattered light, control noise, etc…) and prospects for the future

## Slide 3: Optical configurations to detect gravitational waves
Lecture 1

## Slide 4: Gravitational waves
+
x
All we need to know for this lecture:
  Change in the distance between mirrors
  For km scale distances, and audio frequencies, flat response in frequency
  Differential displacement along orthogonal arms

## Slide 5: Interferometric detectors

## Slide 6: Lasers
Monochromatic light source
Diffraction limited, but we can use a plane-wave approximation for most of the discussion
The Advanced LIGO Pre-Stabilized Laser

## Slide 7: Lasers
Monochromatic light source
Diffraction limited, but we can use a plane-wave approximation for most of the discussion
The Advanced LIGO Pre-Stabilized Laser
LIGO laser power 70 W
Wavelength 1064 nm

## Slide 8: Mirrors
Dielectric coatings
Very low absorption
High optical quality of both substrate and surface
An Advanced LIGO mirror suspended in the vacuum chamber

## Slide 9: Mirrors
Dielectric coatings
Very low absorption
High optical quality of both substrate and surface
An Advanced LIGO mirror suspended in the vacuum chamber

## Slide 10: Mirrors
Dielectric coatings
Very low absorption
High optical quality of both substrate and surface
An Advanced LIGO mirror suspended in the vacuum chamber

## Slide 11: Mirrors
Dielectric coatings
Very low absorption
High optical quality of both substrate and surface
An Advanced LIGO mirror suspended in the vacuum chamber

## Slide 12: Photodetectors
They can detect only the power
Output a current proportional to the impinging laser power
Instantaneous absolute phase of field not accessible
The Advanced LIGO photodiode that detected the first GW

## Slide 13: Photodetectors
They can detect only the power
Output a current proportional to the impinging laser power
Instantaneous absolute phase of field not accessible
The Advanced LIGO photodiode that detected the first GW

## Slide 14: Michelson interferometer
Arguably the most sensitive instrument to detect differential strain
Based on interference of two laser beams propagating in orthogonal directions
The original Michelson and Morley experiment

## Slide 15: Michelson interferometer
Arguably the most sensitive instrument to detect differential strain
Based on interference of two laser beams propagating in orthogonal directions
The original Michelson and Morley experiment

## Slide 16: Michelson interferometer

## Slide 17: Michelson interferometer

## Slide 18: Michelson interferometer

## Slide 19: Michelson interferometer

## Slide 20: Michelson Interferometer

## Slide 21: Response to GW signals
We detect the power at the anti-symmetric port

## Slide 22: Response to GW signals
We detect the power at the anti-symmetric port

## Slide 23: Response to GW signals
We detect the power at the anti-symmetric port

## Slide 24: Response to GW signals
We detect the power at the anti-symmetric port

## Slide 25: Shot noise
Light is quantized
Power is proportional to the number of photons
Uncorrelated events: Poisson’s distribution
The Poisson distribution for an average number of events equal to 3

## Slide 26: Shot noise
Light is quantized
Power is proportional to the number of photons
Uncorrelated events: Poisson’s distribution
The Poisson distribution for an average number of events equal to 3

## Slide 27: Signal to noise ratio
Power at AS port:
Optical gain:

## Slide 28: Signal to noise ratio
Power at AS port:
Optical gain:

## Slide 29: Signal to noise ratio

## Slide 30: How to improve the sensitivity?

## Slide 31: Fabry-Perot resonant cavities

## Slide 32: Fabry-Perot resonant cavities

## Slide 33: Fabry-Perot resonant cavities

## Slide 34: Fabry-Perot resonant cavities

## Slide 35: Fabry-Perot resonant cavities

## Slide 36: Frequency response

## Slide 37: Frequency response

## Slide 38: Frequency response

## Slide 39: Frequency response

## Slide 40: Frequency response

## Slide 41: Cavity pole

## Slide 42: Fabry-Perot Michelson

## Slide 43: Fabry-Perot Michelson

## Slide 44: Power recycling

## Slide 45: Power recycling

## Slide 46: Power recycling

## Slide 47: Power recycling

## Slide 48: Power Recycling

## Slide 49: Power Recycling

## Slide 50: Signal recycling

## Slide 51: Signal recycling

## Slide 52: Detuned cavity

## Slide 53: Signal recycling

## Slide 54: Signal recycling

## Slide 55: Signal recycling

## Slide 56: Signal recycling

## Slide 57: Summary

## Slide 58: Advanced LIGO design

## Slide 59: Next time
Let’s get a bit more realistic: fundamental noise sources
  Quantum noise and squeezing
  Thermal noise and coatings
  Seismic noise
Gabriele Vajente
LIGO Laboratory California Institute of Technology
1200 E. California Blvd.
Pasadena (CA) 91125 – USA
vajente@caltech.edu